## Slide 1: Connect 4 Game

## Slide 2: Team members
Rana Tarek
Afaf Abdelwahab abdelkader
Sayed Ebrahem Sayed
Alaa ahmed EBRAHEM
Zeinab Ahmed younes

## Slide 3: Introduction
This is a connect 4 game with TIVA mc that you can play with another player.
We use interrupt ,timer ,drivers, external switches and LEDs

## Slide 4: Project idea

## Slide 5: Project idea
Project Idea is to create a Connect4 game that can be played on the Nokia 5110 display using the GPIO interrupts for player inputs (x or o).
Initially it prints welcome connect4 on screen, then display the board of the game.
Player’s position can be controlled by switches , players move horizonal using sw1 and vertical using sw2.
Player wins when collecting 4 pieces horizontally ,vertically or diagonally, then the LED will light up.

## Slide 6: Code description

## Slide 7: Drivers
GPIO Driver:
It includes functions to initialize and configure GPIO ports, enable/disable clock for a port, unlock port pins, allow changes to port pins, set analog function, set pin direction, disable alternate function, enable pull-up resistors, enable digital pins, and configure interrupts.
The "GPIO_PORTF_Init"
function: initializes the GPIO port F. It enables the clock for port F, unlocks port F pins, allows changes to specific pins, sets analog function to digital, clears pin control, sets pin directions, disables alternate function, enables pull-up resistors, enables digital pins, configures interrupts for specific pins, sets interrupt priority, and enables interrupt in NVIC.
 The “GPIO_EnablePortClock” function: enables the clock for a specified port.
 The “GPIO_AllowChanges” function: allows changes to the specified pins in a port.

## Slide 8
The “GPIO_SetAnalogFunction” function sets the specified pins in a port to the analog function.
The “GPIO_ClearPinControl” function clears the pin control settings for the specified pins in a port.
The “GPIO_SetPinDirection” function sets the direction (input or output) for the specified pin in a port.
The “GPIO_DisableAlternateFunction” function disables the alternate function for the specified pins in a port.
The “GPIO_EnablePullUp” function enables the pull-up resistor for the specified pin in a port.
The “GPIO_EnableDigital” function enables the digital functionality for the specified pins in a port.
The “GPIO_SetInterruptSense” function sets the interrupt sense (level or edge) for the specified pin in a port.
The “GPIO_SetInterruptBothEdges” function sets whether both edges of the specified pin trigger an.

## Slide 9
Timer
These arrays are used to access the registers for a specific timer.The code includes several functions:
 CLK_Enable_GPTM_Module:Enables the clock for a specific timer.
 Enable_Timer_Number: Enables or disables a specific timer.
 Timer_Number_Option: Selects the timer option (16, 32, or RTC) for a specific timer.
 Timer_Number_Mode: Selects the timer mode (one_shot, periodic, or capture) for a specific timer.
 Timer_Number_Ticks: Loads the number of ticks for a specific timer.
GPTM_Delay_Unit: Implements a delay using the GPTM timer for a specified number of units .
 TIMER_INIT: Initializes the timer by enabling the clock, setting the timer option, mode, and implementing a delay.

## Slide 10: Functions Description
 startingScreen: Initializes the game screen by clearing the Nokia5110 buffer, displaying a welcome message, and setting up a timer.
 printBoard: Prints the game board on the Nokia5110 display by iterating through the board array and setting the corresponding characters at each position.
 changeBoard: Updates the game board by placing a player's piece in the specified column. It finds the lowest empty position in the column and updates the board accordingly.
 hasEmptyCol: Checks if a specified column in the game board has any empty positions. Returns 1 if there is at least one empty position, otherwise returns 0.

## Slide 11: Functions Description
 checkWin: Checks if there is a winning combination on the game board by calling three separate check functions:
 horizontalCheck, verticalCheck, and diagonalCheck. Returns 1 if a win is detected, otherwise returns 0.
 checkFour: Checks if four specified positions on the game board contain the same non-empty character. Returns 1 if they match, otherwise returns 0.
 horizontalCheck: Checks for a winning combination horizontally on the game board by iterating through each row and column.
 verticalCheck: Checks for a winning combination vertically on the game board by iterating through each column and row.
 diagonalCheck: Checks for a winning combination diagonally on the game board by iterating through each row and column and checking both left and right diagonals

## Slide 12: Functions Description
 takeTurn: Allows a player to take their turn in the game. The function waits for button presses (sw1 and sw2) and updates the cursor position accordingly. When sw2 is pressed, it returns the result of changeBoard function, which updates the game board with the player's move.

## Slide 13: Functions Description
 The main() function :
1-Initializes the GPIO port F and sets up the game board (board1) with empty spaces.
2-Initializes the Nokia 5110 LCD display and clears its buffer.
3-Calls the startingScreen() function to display the starting screen.
4-Clears the Nokia 5110 display and calls printBoard(board1) to display the initial game board.
5-Enters a loop that continues until a player wins or the game ends in a tie.
Inside the loop, it takes turns for each player by calling the takeTurn() function and updates the display using printBoard().Checks for a win condition using the checkWin() function.Increments the turn counter and breaks the loop if a win condition is met.
6-fter the loop ends, it displays the final game board and the result (win or tie) on the Nokia 5110 display.

## Slide 14: Functions Description
 GPIOPortF_Handler() function to handle interrupts from switches SW1 and SW2 on port F.
It sets flags sw1_pressed and sw2_pressed and
initializes a timer.

## Slide 15: GitHub link
https://github.com/sayed-zarad/test-project-connect4

## Slide 16: thank you